## Slide 1: Lecture 6 ISA Principles
EE-204 Computer Architecture
Fall 2018

## Slide 2: 3 Type and Size of operands
How is the type specified in instructions? Two options:
Encoding the type of operand in the op-code is the most used method
Tags can be attached to data that can be interpreted by the hardware
Tagged data computers are obsolete
Byte
Half-word (HW)
Word (W)
Single Precision Floating-Point
Double Precision Floating-Point

## Slide 3: 4 Operations in the Instruction Set

## Slide 4: The top 10 instructions for 80x86

## Slide 5: 5 Instructions for Control Flow
Unconditional jump
Jump instruction
Conditional jump
Branch instruction
Four different types of control flow instructions
Conditional branches
Jumps
Procedure Calls
Procedure Returns
Relative Frequency of each of the above events
Conditional branches dominate with the highest frequency of occurrence

## Slide 6: Breakdown of control flow instructions into three classes

## Slide 7: Addressing Modes for Control Flow Instructions
Specifying the destination address
PC-relative method
Provides position independence
For targets not known at compile time
Use register indirect addressing mode
Also useful for four other features
Case or switch statements of programming languages
Virtual functions or methods in object-oriented languages
High-order functions or function pointers in languages
Dynamically shared libraries
PC-relative target address: 4 to 8 bits
75% of all branch are in forward direction

## Slide 8: Conditional Branch Options
How to specify branch conditions?
Three techniques are used to specify branch condition
Properties of branch
A large number of comparisons are simple tests
A large number of comparisons are with zero

## Slide 9: The major methods for evaluating branch conditions

## Slide 10: Condition Code
CF - carry flag
PF - parity flag
ZF - zero flags
SF - sign flag
OF - overflow flag

## Slide 11: Condition Register
mov r4, #10
loop_label:
bl do_something
sub r4, r4, #1
cmp r4, #0
bne loop_label

## Slide 12: Compare and Brach
beq $6, $8, there (branch if equal)
bne $6, $8, here (branch if not equal)

## Slide 13: Procedure Invocation Options
Return Address?
Save in a special link register or save in a GPR or on runtime stack
Saving of other registers?
There are two basic conventions in use to save registers:
Caller saving
Callee saving

## Slide 14: Caller saving Vs. Callee saving
Caller saving means that the calling procedure must save the registers that it wants preserved for access after the call, and thus the called procedure need not worry about registers.
Callee saving is the opposite: the called procedure must save the registers it wants to use, leaving the caller unrestrained.

## Slide 15: Example
Suppose we have a procedure P1 that calls procedure P2, and both procedures manipulate the global variable x.
If P1 had allocated x to a register, it must be sure to save x to a location known by P2 before the call to P2.
In the cases where either convention could be used, some programs will be more optimal with callee save and some will be more optimal with caller save.

## Slide 16: Frequency of different types of compares in conditional branches

## Slide 17: Encoding an Instructions Set
Three popular choices for encoding of instruction sets
Variable length
Fixed length
Hybrid

## Slide 18
More than 3 operands—some CISC machines permit a variety of addressing modes that allow more than 3 operands (registers or memory accesses), such as the VAX "POLY" polynomial evaluation instruction.

## Slide 19: Just an Example