## Slide 1: EE 204 – Computer Architecture
Lecture # 7

## Slide 2: Trends in Technology
Five implementation technologies, which change at dramatic pace, are critical to modern implementations:
Integrated circuit logic technology:
A growth rate in transistor count on a chip of about 40% to 55% per year, or doubling every 18 to 24 months. This trend is popularly known as Moore’s law.

## Slide 3: Trends in Technology
Semiconductor DRAM (dynamic random-access memory):
Capacity per DRAM chip has increased by about 25% to 40% per year recently, doubling roughly every two to three years.

## Slide 4: Trends in Technology
Semiconductor Flash (electrically erasable programmable read-only memory)
This nonvolatile semiconductor memory is the standard storage device in PMDs, and its rapidly increasing popularity has fueled its rapid growth rate in capacity.
Capacity per Flash chip has increased by about 50% to 60% per year recently, doubling roughly every two years.

## Slide 5: Trends in Technology
Magnetic disk technology:
Prior to 1990, density increased by about 30% per year, doubling in three years.
It rose to 60% per year thereafter, and increased to 100% per year in 1996.
Since 2004, it has dropped back to about 40% per year, or doubled every three years. Disks are 15 to 25 times cheaper per bit than Flash.

## Slide 6: Trends in Technology
Network technology:
Network performance depends both on the performance of switches and on the performance of the transmission system.

## Slide 7: Trends in Power and Energy
Today, power is the biggest challenge facing the computer designer for nearly every class of computer.
First, power must be brought in and distributed around the chip, and modern microprocessors use hundreds of pins and multiple interconnect layers just for power and ground.
Second, power is dissipated as heat and must be removed.

## Slide 8: Power and Energy: A Systems Perspective
How should a system architect or a user think about performance, power, and energy? From the viewpoint of a system designer, there are three primary concerns.

## Slide 9: First Concern

## Slide 10: 2nd Concern

## Slide 11: 3rd Concern

## Slide 12: Example for 3rd Concern
Thus, if we want to know which of two processors is more efficient for a given task, we should compare energy consumption (not power) for executing the task.
For example, processor A may have a 20% higher average power consumption than processor B, but if A executes the task in only 70% of the time needed by B, its energy consumption will be 1.2 × 0.7 = 0.84, which is clearly better.

## Slide 13: Methods to Improve Energy Efficiency
Do nothing well:
Most microprocessors today turn off the clock of inactive modules to save energy and dynamic power.
Dynamic Voltage-Frequency Scaling (DVFS):
Personal mobile devices, laptops, and even servers have periods of low activity where there is no need to operate at the highest clock frequency and voltages.

## Slide 14: Methods to Improve Energy Efficiency
Design for typical case:
Given that PMDs and laptops are often idle, memory and storage offer low power modes to save energy.
For example, DRAMs have a series of increasingly lower power modes to extend battery life in PMDs and laptops, and there have been proposals for disks that have amode that spins at lower rates when idle to save power.
Overclocking:
Intel started offering Turbo mode in 2008, where the chip decides that it is safe to run at a higher clock rate for a short time possibly on just a few cores until temperature starts to rise.