## Slide 1: EE 204 – Computer Architecture
Lecture # 9

## Slide 2: Today’s Topic
CPU Performance Equation
  Analysis of CPU time
  Basic Performance Equation
  Analysis of Basic Performance Equation
  Calculating Instruction Count
  Calculating CPI
  Examples
  BIG Picture – Processor Performance Equation
  How Basic Performance Equation is affected by Algorithm, Compiler, Programming Language, Instruction Set Architecture?

## Slide 3
* CPU time also called CPU execution time

## Slide 4: CPU (Execution) Time and its Factors
Ref. Ch # 4 - Computer Organization Design by Patterson and Hennessey
X
Hardware designer can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program.
The designer often faces a trade-off between the number of clock cycles needed for a program and the length of each cycle. Many techniques that decrease the number of clock cycles also increase the clock cycle time.

## Slide 5: Basic Performance Equation
Ref. Ch # 4 - Computer Organization Design by Patterson and Hennessey
X
X
X
Therefore three factors effect CPU time:
Instruction count of the executing program
CPI (Average Clock cycles Per Instruction. e.g. ADD, MOV, MUL)
Clock cycle time (Clock rate = 1 / Clock cycle time)

## Slide 7: Calculating Instruction Count
Use of software tools to profile the execution on actual processor.
Different simulation techniques and queuing theory could be used to obtain values for components of the execution (CPU) time.
Modern processors have on-chip hardware counters to record a variety of measurements, including the number of instructions executed, CPI, and often, the sources of performance loss.
Ref. Ch # 4 - Computer Organization Design by Patterson and Hennessey

## Slide 12: Processor Performance Equation– The BIG Picture

## Slide 14: Principle of Locality
The principle of locality states that programs access a relatively small portion of their address space at any instant of time, just as you accessed a very small portion of the library’s collection.

## Slide 15: Types of Locality
Temporal locality (locality in time): If an item is referenced, it will tend to be referenced again soon. If you recently brought a book to your desk to look at, you will probably need to look at it again soon.
Spatial locality (locality in space): If an item is referenced, items whose addresses are close by will tend to be referenced soon. For example, books on the same topic are shelved together in the library to increase spatial locality.

## Slide 16: Dependability
Dependability is defined as the quality of being able to be counted on or relied upon.
Service level agreements (SLAs)
Service level objectives (SLOs)

## Slide 17: Mean Time to Failure (MTTF)
Mean time to failure (MTTF) is the length of time a device or other product is expected to last in operation.
MTTF is one of many ways to evaluate the reliability of pieces of hardware or other technology.
Mean time between failures (MTBF) is simply the sum of (MTTF + MTTR)

## Slide 18: Availiability